SALT simulations
Faculty of Physics and Applied Computer Science
AGH University of Science and Technology
LHCb UT May 2018

---
Schematic simulations
Transient

---
Simulations of SALT 2.5
Schematic plus main resistances
- Simulations of 128 mixed-mode channels (FE+ADC), Digital part not included. Simulator used ++APS(Sampled), conservative
- Simulated configurations of Preamp gnd:
  - Default, with Out_gnd (vssa_pre)
  - With Out_gnd(vssa_pre) and In_gnd(vssai)
  - With In_gnd(vssai)
- In simulations the resistances of power/gnd network are added artificially
- Added resistances:
  - General network (common for all channels, horizontal in layout) – res_vdda_presh=200m, res_vdda_adc=200m, res_vdda_ref=200m, res_vssa_pre=100m, res_vdda_sh=100m, res_vdda_adc=300m)
  - Inter-channel power network (additive to general, in layout vertical going up/down from the middle) – r_vdda=1m, r_vdds2d=8m, r_vddadc=3m, r_vrefd=14.5m, r_vssai=2m, r_vssa=2m, r_vsss2d=8m, r_vssadc=3m)

---
Schematic Simulations of SALT 2.5
S2d out (Only Out_gnd, Cdet 12pF, Ipre 4/15)
- Two pulses for Ipre=4/15
- Other channels with baseline oscillations within ~1LSB

---
S2d out (Out_gnd&In_gnd, Cdet 12pF, Ipre 4/15)
- Two pulses for Ipre=4/15
- Other channels with baseline oscillations within ~1LSB

---
S2d out (Only In_gnd, Cdet 12pF, Ipre 4/15)
- Two pulses for Ipre=4/15
- Other channels with baseline oscillations within ~1LSB

---
S2d out (Only Out_gnd, Cdet 12pF, Ipre 15)
Comparison: ++APS_Sampled vs APS
- Blue with APS, Pink with ++APS_Sampled
- Visible difference in pulse amplitude but not in baseline oscillations

---
S2d out (Only Out_gnd, Cdet 12pF, Ipre 15)
Pulse injection: External vs Calibration
First pulse injected externally, next two from Calibration

---
S2d out (Only Out_gnd, Cdet 12pF, Ipre 15)
Power supply 1.1 V, 1.2V, 1.3V
- Higher supply higher amplitude (and faster)
- Baseline oscillations similar

---
S2d out (Only Out_gnd, Cdet 12pF, Ipre 15)
Inductance per power supply bond 2nH, 4nH
No significant difference between 2nH and 4nH

---
S2d out (Only Out_gnd, Cdet 12pF)
vcm = 0,16,32,63
For 16,32 ok, lower for 63, very low for 0

---
Preamp out (Only Out_gnd, Cdet 12pF)
Ipre = 4,8,15,30
- Faster pulse for higher Ipre
- Baseline DC change of 1-2mV

---
Simulations of SALT 2.5
Schematic plus main resistances
DC measurements
- Default settings are:
  - Ipre=15
  - Ikrum=4
  - Ivcm=32
  - Ish=12
  - Is2d=12
  - Ibase=128
  - Ipulse=15
- ..

---
Ivdda (Only Out_gnd, Cdet 12pF)
Ipre=4,8,15,30, other settings default

---
Ivdda (Only Out_gnd, Cdet 12pF)
Ish=3,6,12, other settings default

---
Ivdda (Only Out_gnd, Cdet 12pF)
Ivcm=0,16,32,63, other settings default
Highest current for highest (63) setting

---
S2d out MC (Cdet 12pF, Ipre 15)
The S2D(differentially) DC baseline stays in the range +-130mV

---
Simulations of SALT 2.5
Effects of internal inductances and their couplings
- The main effect of internal inductances may come from long (~2.5mm) horizontal lines of ADC power supply and Preamp ground which are placed in parallel, have widths of 100-200um and are separated by less than 50um.
- First order estimation of the inductance of ADC power or Preamp gnd line is about 1.5-1.7nH for each of them.
- First order estimation of coupling between ADC power and Preamp gnd lines is huge, of about 50%. The estimation is based on the figure/equation from next slide. We suspect that in reality, because there are many other metal lines around, it is significantly less.

---
Simulations of SALT 2.5
Effects of internal inductances and their couplings

---
How inductances and their couplings are simulated
- Top left (Salt_Power_Bond…) block contains bond inductances and series resistances of long power/gnd lines in SALT2.5.
- Bottom - SALT2.5 (only the side with power supply network is seen)
- Inductances Lvdda, Lvddadc, …, simulate internal inductances (e.g. horizontal power/gnd lines). For 1st appr. 2nH was used.
- Top right - Lcouplings. 3 are seen here: vddadc-vssa_pre, vddadc-vssa, vddadc-vdda. Each of them may be set between -1,+1. For 1st simulation only vddadc-vssa_pre was used.
- Next slide shows the zoom of this schematic...

---
How inductances and their couplings are simulated

---
S2Diff out vs Lcoup (Vdd_ADC, Vssa_Pre)
(Only Out_gnd, Cdet 12pF)
- Internal inductance of 2nH for Vdd_ADC and Vss_Pre added
- Lcoupling between Vdd_ADC and Vss_Pre -0.1, -0.05, -0.03, 0.0

---
S2Diff out vs Lcoup (Vdd_ADC, Vssa_Pre) vs Ipre
(Only Out_gnd, Cdet 12pF)
- Internal inductance of 2nH for Vdd_ADC and Vss_Pre added
- Lcoupling Vdd_ADC and Vss_Pre -0.05, 0.0, Ipre 4, 15
- Ipre has big effect on oscillations amplitude!

---
Simulations of SALT 2.5
Effects of internal inductances and their couplings
- In addition to previous simulations, the 2nH internal inductance has been added to all power/gnd lines: Vdda_ADC, Vrefd, Vssa_adc, Vdda, Vssa, Vssa_Pre
- Different coupling configurations will be studied...

---
S2Diff out (Lcoup -0.1,0, Cdet 12pF)
(Vdd_ADC coupled to Vssa_Pre or Vssa)
- Lcoupling to: Vssa_Pre, Vssa, No coupling
- Coupling to Vssa_pre is dominant!

---
Simulations of SALT 2.5
Effects of internal inductances and their couplings
- An attempt to estimate the effect of inductive coupling between vertical power/gnd lines was made…
- The same as before 2nH inductances were used for vertical lines, although vertival length is about 1cm (4 x more than horizontal). On the other hand not whole ADC current flows through the whole length…
- In the layout the lines (from the left) go in order: Vssa_pre, Vdda, Vssa, Vdda, ADC power and gnd lines
- Since the dominant effect comes from Vssa_pre sensitivity, it was assumed that Vdda_ADC couples to Vdda and then Vdda to Vssa_pre. The same coupling strength for both pairs was used.
- In these simulations horizontal coupling/inductances were OFF (zero).

---
S2Diff out (Cdet 12pF)
Vdd_ADC coup. to Vdda and Vdda to Vssa_Pre
- Lcoupling: -0.5, -0.2,-0.1,0
- Effect is still there but higher coupling (>0.2) is needed

---
Simulations of SALT 2.5
Why we see the effects of internal L/Lcouplings while others do not ?
- Ivddadc current changes by ~90mA during 25ns period !
- Effect of Lcoupling is multiplied by huge current changes !